## Slide 1: State Construction Office Update 2020 ACAF Conference
Richard Hewitt, P.E.
State Construction Pavement Engineer
FDOT State Construction Office

## Slide 2: Construction Update Overview
Specification Changes
Limited Access Roadway Smoothness
  IRI Projects
  Ride Number vs IRI Projects
Non-Limited Access Roadway Smoothness System
e-Ticketing & Implementing Changes

## Slide 3: Specification Changes

## Slide 4: 327-3.1.1
Allow Traffic On Milled Surface Up To 3 Days Before Paving
Submitted For July 2021 Workbook
  Going Through Internal & Industry Review
Allowed Upon Engineer Approval, Provided There Are
  Continuous, Longitudinal Milling Striations
  No Drop Off or Safety Issues
  No Drainage Issues
If Requirements Not Met, Go Back to Pave Day After Milling
Photos of Acceptable & Unacceptable Striations
  https://www.fdot.gov/programmanagement/implemented/urlinspecs/milling-patterns

## Slide 6: Acceptable Milling Striations

## Slide 7: Unacceptable Milling Striations

## Slide 8: Section 330 & 334
Raised Crosswalks & Speed Tables
  Added to Straightedge Testing Exceptions in 330-9.4.5.2
    3/8” Deficiency Requirement for Objectionable Areas
  Added to Density Testing Exceptions in Section 334-5.1.2

## Slide 9: Raised Crosswalks
Thanks to ACAF & ACAF Contractors Who Provided Constructability Input During Creation of Developmental Standard Plan 520-030 & Changes to Standard Specifications 330 & 334
  Mark Musselman (ACAF)
  Rick Crocker (Preferred Materials)
  Felipe Jaramillo (Ajax Paving)
  Julio Legañoa (Halley Engineering Contractors)
  Chris Harris (Anderson Columbia)
  Scott Fowler (Ranger Construction)
  Pete Fronczak & Joe Meier (Middlesex Construction)

## Slide 10: Limited Access Roadway Smoothness IRI Specification Projects

## Slide 11: 2018 Limited Access - IRI Spec Projects vs Interstate (2005 to 2010)
Chart: IRI Distribution
| 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 59 | 61 | 62 | 63 | 68 | 69 | 71 | 76
Limited Access Roads - Acceptance 2018 | 0.20243 | 0.40486 | 0.40486 | 1.2146 | 2.2267 | 2.834 | 4.4534 | 6.6802 | 6.0729 | 8.502 | 3.6437 | 6.2753 | 6.2753 | 6.4777 | 6.0729 | 3.8462 | 3.8462 | 3.8462 | 2.834 | 3.8462 | 1.8219 | 2.6316 | 2.6316 | 1.6194 | 1.2146 | 1.2146 | 1.8219 | 0.40486 | 0.40486 | 0.40486 | 1.0121 | 1.417 | 0.60729 | 0.20243 | 0.40486 | 0.20243 | 0.20243 | 0.40486 | 0.40486 | 0.20243 | 0.20243 | 0.20243 | 0.20243 | 0.20243
2018 Limited Access IRI Projects
Original Interstate Data 2005-2010

## Slide 12: 2018 Limited Access - IRI Spec Projects
Year | District | County | FIN | SR | Lane Miles | Incentive | Incentive per Lane Mile | Avg. IRI | Aggregate
2018 | 8 | Okeechobee | 435166-1 | 91 | 14.0 | $20,890 | $1,493 | 36 | Limestone
 | 8 | Indian River | 435168-1 | 91 | 8.0 | $11,020 | $1,373 | 37 | Limestone
 | 8 | Okeechobee | 435165-1 | 91 | 15.5 | $20,993 | $1,356 | 37 | Limestone
 | 8 | Indian River | 435167-1 | 91 | 10.9 | $18,267 | $1,671 | 34 | Limestone

## Slide 13: 2018 IRI Spec Project Overview
4 Projects
Lowest Project Average IRI = 34 in/mile
Highest Project Average IRI = 37 in/mile
All 4 Limestone Projects Received Incentives
Average Incentive = $1,473 per Lane Mile
Total Incentives = $71,170

## Slide 14: 2019 Limited Access - IRI Spec Projects vs Interstate (2005 to 2010)
Chart: IRI Distribution
2019 Limited Access IRI Projects
Original Interstate Data 2005-2010

## Slide 15: 2019 Limited Access - IRI Spec Projects
Year | District | County | FIN | SR | Lane Miles | Incentive | Incentive per Lane Mile | Avg. IRI | Aggregate
2019 | 8 | Osceola | 442901-8 | 91 | 3.8 | $(4,554) | $(1,186) | 60 | Granite
 | 4 | Martin | 434273-1 | 9 | 46.3 | $15,188 | $328 | 46 | Limestone
 | 4 | Palm Beach | 434273-2 | 9 | 11.6 | $5,440 | $467 | 44 | Limestone
 | 4 | Palm Beach | 436521-1 | 91 | 24.1 | $28,734 | $1,193 | 38 | Limestone
 | 8 | Lake | 437988-1 | 91 | 18.4 | $6,557 | $356 | 43 | Granite
 | 4 | Palm Beach | 427516-1 | 9 | 35.2 | $32,550 | $924 | 40 | Limestone

## Slide 16: 2019 IRI Spec Project Overview
6 Projects
Lowest Project Average IRI = 38 in/mile
Highest Project Average IRI = 60 in/mile
5 out of 6 Projects Received Incentives
All Limestone Projects Received Incentives
Average Incentive = $355 per Lane Mile
Total Net Incentives = $83,915

## Slide 17: 2020 Limited Access – IRI Spec Projects vs Interstate (2005 to 2010)
Chart: IRI Distribution

## Slide 18: 2020 Limited Access-IRI Spec Projects (Jan – mid Nov)
Year | District | County | FIN | SR | Lane Miles | Incentive | Incentive per Lane Mile | Avg. IRI | Aggregate
2020 | 8 | Brevard | 439479-1 | 528 | 61.4 | $27,698 | $451 | 44 | Granite
 | 7 | Hillsborough | 436588-1 | 400 | 156.2 | $109,970 | $704 | 42 | Granite
 | 8 | Palm Beach | 437991-1 | 91 | 33.5 | $27,348 | $817 | 41 | Limestone
 | 8 | Orange | 439478-1 | 528 | 37.6 | $45,086 | $1,198 | 38 | Both
 | 8 | Osceola | 432826-4 | 91 | 46.6 | $78,610 | $1,689 | 34 | Granite
 | 8 | Osceola | 435169-1 | 91 | 5.7 | $9,749 | $1,721 | 34 | Granite
 | 7 | Hillsborough | 437312-1 | 93 | 72.7 | $186,352 | $2,563 | 24 | Granite

## Slide 19: 2020 IRI Spec Project Overview (Jan – mid Nov)
7 Projects
Lowest Average Project IRI = 24 in/mile
  New State Record!
Highest Average Project IRI = 55 in/mile
All 7 Projects Received Incentives
One Project Received Consistency Incentive
Avg Incentive = $1,050 per Lane Mile
Total Incentives = $353,382
  Does Not Include Project Wide Consistency Incentive

## Slide 20: Jan 2018 – mid Nov 2020 Limited Access - IRI Spec Project Overview
16 out of 17 Projects Received Incentives
All Limestone Projects Received Incentives
Total Net Incentives Paid = $508,467
Smoothness Incentive Spec is a Positive
  Incentives for Smooth Paving
  Smoother Asphalt Pavements

## Slide 21: Limited Access Roadway Smoothness Ride Number vs IRI Projects

## Slide 22: 2018 Limited Access - RN Spec vs Interstate (2005 to 2010)
2018 Limited Access IRI Projects
Original Interstate Data 2005-2010
Chart: International Roughness Index (inch/mile)

## Slide 23: 2018 Limited Access - IRI Spec Projects vs Interstate (2005 to 2010)
Chart: IRI Distribution
| 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 59 | 61 | 62 | 63 | 68 | 69 | 71 | 76
Limited Access Roads - Acceptance 2018 | 0.20243 | 0.40486 | 0.40486 | 1.2146 | 2.2267 | 2.834 | 4.4534 | 6.6802 | 6.0729 | 8.502 | 3.6437 | 6.2753 | 6.2753 | 6.4777 | 6.0729 | 3.8462 | 3.8462 | 3.8462 | 2.834 | 3.8462 | 1.8219 | 2.6316 | 2.6316 | 1.6194 | 1.2146 | 1.2146 | 1.8219 | 0.40486 | 0.40486 | 0.40486 | 1.0121 | 1.417 | 0.60729 | 0.20243 | 0.40486 | 0.20243 | 0.20243 | 0.40486 | 0.40486 | 0.20243 | 0.20243 | 0.20243 | 0.20243 | 0.20243
2018 Limited Access IRI Projects
Original Interstate Data 2005-2010

## Slide 24: 2019 Limited Access - RN Spec vs Interstate (2005 to 2010)
Chart: International Roughness Index (inch/mile)

## Slide 25: 2019 Limited Access - IRI Spec Projects vs Interstate (2005 to 2010)
Chart: IRI Distribution
2019 Limited Access IRI Projects
Original Interstate Data 2005-2010

## Slide 26: 2020 Limited Access - RN Spec vs Interstate (2005 to 2010)
Chart: International Roughness Index (inch/mile)

## Slide 27: 2020 Limited Access – IRI Spec Projects vs Interstate (2005 to 2010)
Chart: IRI Distribution

## Slide 28: RN vs IRI Project Summary
Difference in IRI Average Between RN & IRI Projects
  2018
    49 - 36 = 7 IRI Points Smoother on Incentive Projects
  2019
    52 - 43 = 9 IRI Points Smoother on Incentive Projects
  2020 (Jan – mid Nov)
    53 - 43 = 10 IRI Points Smoother on Incentive Projects

## Slide 29: RN vs IRI Spec Summary
IRI Incentive/Disincentive Spec Projects
  Paved Smoother than Projects with Ride Number Spec
  Incentivizes Contractors to Pave Smoother
  Incentives Benefit Contractors, FDOT, & Travelling Public

## Slide 30: Non-Limited Access Roadway Smoothness System

## Slide 31: Non-Limited Access IRI-Based Smoothness System
Writing Developmental Smoothness Specification
  Non-Limited Access Roads
    Design Speed 55mph & Greater
      i.e. Projects Currently Laser Tested with Ride Number
  IRI-Based Smoothness Specification
  Smoothness Incentives & Disincentives

## Slide 32: Non-Limited Access IRI-Based Smoothness System
Based on Past Construction Acceptance Data
  Same as Current Limited Access IRI Specs Are
However, Split Into Multiple Classes to
  Account for Level of Ease or Difficulty to Pave Smoothly
  Appropriately Evaluate Construction Acceptance
  Fairly Incentivize Smoothness

## Slide 33: Non-Limited Access vs Limited Access Roads
Chart: IRI Distribution
Non-Limited Access
2014-2019
IRI Average = 46
Std. Dev. = 12
Limited Access
2005-2010
IRI Average = 48
Std. Dev. = 13

## Slide 34: IRI Pay Adjustment Limits
Class | IRI Pay Adjustment Limits |  |  | 
 | Incentive | Full Pay | Disincentive | R&R
1 | ≤ 36 | 37 - 42 | 43 - 95 | >95
2 | ≤ 42 | 43 - 55 | 56 - 95 | >95
3 | ≤ 52 | 53 - 62 | 63 - 110 | >110
4 | ≤ 62 | 63 - 85 | 86 - 125 | >125
5 | ≤ 85 | 86 - 105 | 106 - 125 | >125

## Slide 35: Lane Miles per Class & District
Lane-Miles |  |  |  |  |  | 
District | Class 1 | Class 2 | Class 3 | Class 4 | Class 5 | Total
1 | 207 | 343 | 212 | 74 | 1 | 838
2 | 626 | 487 | 158 | 41 | 0 | 1,313
3 | 1,014 | 408 | 24 | 1 | 0 | 1,447
4 | 4 | 263 | 70 | 72 | 0 | 409
5 | 71 | 202 | 264 | 19 | 1 | 558
6 | 0 | 44 | 100 | 58 | 1 | 203
7 | 16 | 214 | 379 | 45 | 0 | 655
Total | 1,939 | 1,961 | 1,208 | 310 | 3 | 5,421

## Slide 36: Net Incentive per Lane Mile - Per Class & District
Incentive/Lane Mile |  |  |  |  |  | 
District | Class 1 | Class 2 | Class 3 | Class 4 | Class 5 | Total
1 | $25 | $133 | $25 | $649 | -$305 | $124
2 | $20 | $95 | $221 | $538 | $0 | $88
3 | $44 | $55 | $604 | $0 | $0 | $56
4 | $690 | $130 | $202 | $37 | $0 | $131
5 | -$25 | $171 | $199 | $456 | -$136 | $169
6 | $0 | $3 | $75 | $435 | $874 | $166
7 | -$114 | $119 | $352 | $372 | $0 | $266
Total | $640 | $706 | $1,678 | $2,487 | $432 | $121

## Slide 37: Net Incentive per Class & District 2014-2019 Data
District | Incentive | Lane Miles | Incentive/ Lane Mile
1 | $104,057 | 837 | $124
2 | $115,897 | 1,313 | $88
3 | $81,014 | 1,447 | $56
4 | $53,396 | 409 | $131
5 | $94,085 | 558 | $169
6 | $33,655 | 203 | $166
7 | $174,167 | 655 | $266
Total | $656,271 | 5,421 | $121

## Slide 38: Non-Limited Access IRI-Based Smoothness System
Currently Writing Developmental Specifications
Next Steps
  Try Dev Spec on Pilot Projects Throughout the State
  Continue Smoothness Committee/Industry Discussion
End Goal
  Move to IRI-based Standard Specification for All Laser Tested Roads
  Eliminate Ride Number & Straightedging of Laser Tested Areas

## Slide 39: Smoothness Data & Analysis
Thanks to Everyone in the Pavement Materials Division of the State Materials Office for Collecting & Analyzing the IRI & RN Data
Special Thanks to Mateo Carvajal of the State Materials Office for the Data Analysis, Tables, & Graphs Provided for the Smoothness Committee & This Presentation

## Slide 40: e-Ticketing

## Slide 41: Contactless Ticketing & e-Ticketing
Implemented Contactless Ticketing In Response to COVID-19
  April 20, 2020
Over 80% of ACAF Contractors Using e-ticketing

## Slide 42: e-Ticketing Advantages
Advanced Mix & Truckload Information
Better Project Tracking
Increased Oversight
  View Paving Progress on Multiple Projects by Phone, Tablet, or Computer
Fleet Management
Electronic Data

## Slide 43: e-Ticketing
Very Few Problems
  Outstanding, Considering the Immediate, Statewide Implementation
Thanks to Contractors, e-Ticketing Vendors, CEI’s & FDOT Personnel Who Made Statewide Asphalt e-Ticketing Implementation Successful
Let’s Continue Working Together To Quickly Implement Changes that Benefit Asphalt Contractors & FDOT
  Regardless of How Challenging or Risky the Change Appears at First

## Slide 44: Questions?
Richard Hewitt, P.E.
  State Construction Pavement Engineer
  State Construction Office
(386) 943-5305 (office)
richard.hewitt@dot.state.fl.us