## Slide 1: Mobile home repairs

## Slide 2: SBS ROOFING (Styrene-Butadiene-Styrene) Self Adhering Cap Sheet

## Slide 3: One Piece Installation Page 115
Measure and cut the pieces, they will run down the wall 3-4”
Position and stick first piece down
Use roller to apply pressure to whole piece
The next piece should cover the sticky tab of the first
Repeat for length of roof

## Slide 4: Two Piece Installation Page 117
All pieces on one side will be on the bottom of the overlap
Stick the and roll the first piece
  Overhang 6” at ridge
Overlap the second piece over stick tab and repeat for length of roof
Follow the same process on the other side

## Slide 5: Vent Pipes Page 119
If possible, cut a hole and slide SBS over pipe and use boot
Otherwise use relief cut and cover with a small SBS square

## Slide 6: Termination Bars Page 120
Termination bar is installed around the top of the mobile home walls to hold down SBS
If overhang is built, attach termination bar to that. If no overhang, attach it to the top plate of wall
Use smaller sections on the rounded end of the mobile home

## Slide 8: Termination Bar Example

## Slide 9: Exposed Seam

## Slide 10: SBS Roof Example

## Slide 11: SBS Roof Example

## Slide 12: Construction Corner
SBS Instructional Video

## Slide 13: “HUG SYSTEMS”

## Slide 14: System in Progress

## Slide 15: Frame Out Underpinning
Install bottom plates
Install vertical framing members

## Slide 17: Build Out Overhang
The overhand prevents water from running down the wall

## Slide 20: Install Flashing and Vinyl Siding

## Slide 25: Things to watch for
Wires!
Details around windows
Appropriate spacing on skirting/underpinning framing
Make sure crawlspace is vented!
  The minimum net area of ventilation opening must not be less than 1 square foot for each 150 square feet of under-floor space area.

## Slide 33: Preliminary Data

## Slide 34: Mobile Home Ceiling Repair
Construction Corner Video

## Slide 35: Questions?