## Slide 1: A new Drumbeat! Direct Potable Reuse
Jennifer West, Managing Director
February
WateReuse California

## Slide 2: CALIFORNIA’S WATER SUPPLY STRATEGY Adapting to a Hotter, Drier Future
New Goals for Recycled Water
800,000 AFY by 2030
1.8 MAF by 2040
Water Board “Strike Team” assessing where the state will be in meeting these goals and challenges – beyond funding!

## Slide 3
Chart: 
beyond | 1800000
WSS Recycled Water Goals
1.8M AFY
732K AFY
800K AFY
2021
2040
2030
Thank you DWQ, Water Board for the graphic!

## Slide 4
2019 - 2021 Recycled Water Use Category
Chart: 
| Agricultural Irrigation | Landscape & Golf Course Irrigation | Industrial & Commercial Application | Geothermal Energy Production | Potable Uses | Other Non-Potable Uses
2019 | 143000 | 160000 | 103000 | 18000 | 176000 | 85000
2020 | 193000 | 206000 | 110000 | 13000 | 177000 | 31000
2021 | 190000 | 202000 | 106000 | 13000 | 183000 | 38000
Other Non-Potable Uses
Potable Uses
Agricultural Irrigation
Landscape & Golf Course Irrigation
Industrial & Commercial Application
Geothermal Energy Production
2019 - 2021
AFY rounded to the nearest 1,000
Acre-feet per year (AFY)

## Slide 6: The Path to Direct Potable Reuse

## Slide 7: Direct Potable Reuse Adoption Timeline
April: Release of New DPR Draft
April 45 day comment period -- board workshop
Dec. 31 Board adopts regulations
Summer: Expert panel approves regulations

## Slide 8: DPR Pathogen Control
Virus
Giardia
Cryptosporidium
12
10
10
Groundwater
Recharge
12 to 14
10 to 12
10 to 12
Surface Water
Augmentation
20
14
15
Direct Potable
Reuse
Can only drop below these levels 10% of the time. Most design to exceed these levels
20
14
15
16
10
11
Acceptable operation for 24 hours
within 4-log buffer
Within 60 minutes, notify State Board and each public water system
Notes: Because of the challenging nature of pathogen detection, particu
larly in highly treated water, the drinking water industry has histori-
cally relied on a log removal value (LRV) framework to ensure adequate
protection of public health (Pecson et al., 2015).

## Slide 9: Expand DPR by Using New Pathogen Research
  Use new dataset from DPR Research “DPR 2” and other high quality historical datasets to develop removal requirements
  Change minimum log removal targets for pathogens from:
  16/10/11 13/10/10
  13 log removal equates to 99.999999999% removal
Virus

## Slide 10: Need Broad Alternatives Clause
Requirement
Alternative
Independent advisory panel
Public Meeting
Written Approval
Need broad alternative clause same as other potable reuse regulations: Now only applies to chemical requirements
Allows DPR regulations to adapt over time to new research and project experience
Requires equivalent or better levels of performance to protect public health
Demonstration
Notes: There are no projects in the ground so how do we know what flexibility we may need for the future. For example pathegen, source control monitoring and staffing

## Slide 11
Questions?