## Slide 1: Kern Fan Groundwater Storage Project Water Storage Investment Program Success February 28, 2019

## Slide 2: Kern Fan Project Highlights
A groundwater storage project in Kern County that will:
    Store water otherwise lost to ocean
    Provide water supply benefits
    Improve operational flexibility in the State’s water system
    Provide benefits to endangered species
Joint implementation by IRWD and Rosedale-Rio Bravo Water Storage District
Sources of water:
  Unallocated SWP Article 21 water
  Estimated Project Cost: $172 million
  Awarded $67.5 million in Prop 1 funds
  Water Storage Investment Program (WSIP)

## Slide 3: WSIP Grant Application Process
Applications submitted: August 2017
Basic eligibility determinations: September 2017
Public benefit ratios and appeals: April 2018
Project scoring and technical review: May 2018
Maximum conditional funding eligibility determinations: July 2018
      California Agencies involved:
        California Water Commission
        Department of Water Resources
        Department of Fish and Wildlife
      Challenges:
        Valuing water for quantifying benefits
        Providing ecosystem benefits to the Delta

## Slide 4: Consulting Firms Used in Application Process
CALSIM II modeling of SWP and Kern Fan Project
  MBK Engineers
Fish and wildlife modeling and analysis
  Cramer Fish Sciences
Economic modeling and analysis
  M.Cubed
Engineering and cost estimating
  Dee Jaspar & Associates

## Slide 5: Kern Fan Project Location
1,200 acres of land well-suited for groundwater recharge, storage, and recovery
Overlays the Kern County Groundwater Sub-basin of the San Joaquin Valley
Strategically located near federal, state, and local water conveyance facilities

## Slide 6: Proposed Kern Fan Project Facilities
Conveyance
  New turnout from the California Aqueduct
  Up to 10-mile canal with up to 500-cfs capacity
Recharge
  1,200 acres of recharge basins
  Up to 100,000 AF annually
Storage
  100,000 AF
Recovery
  12 wells, up to 70 cfs
  50,000 AF per year

## Slide 7: Preliminary Location of Proposed Project Facilities

## Slide 8: Kern Fan Project Benefits
Emergency Response:
Droughts and Delta levee failures
Ecosystem Benefits:
Reduces stress on the SWP to protect salmon
Flow for chinook salmon and green sturgeon
Intermittent wetland habitat

## Slide 9
Project will store State Project water otherwise lost to the ocean
  Unallocated Article 21 water
    Via Dudley Ridge Water District & Kern County Water Agency
  New water supply
Recharge up to 70,000 acre-feet during wet years
No impacts to State Water Project or contractors
No changes to water rights or contracts
Kern Fan Project Operations

## Slide 10: Kern Fan Project Operations

## Slide 11: Kern Fan Project Timeline

## Slide 12: Contact Information
Irvine Ranch Water District:
Paul Weghorst
Executive Director of Water Policy
Office: (949) 453-5632
weghorst@irwd.com
Rosedale-Rio Bravo
Water Storage District:
Eric Averett
General Manager
Office: (661) 589-6045
eaverett@rrbwsd.com