## Slide 1: Colorado River Basin Drought Contingency Plan Status
Urban Water Institute’s
Spring Water Conference
Palm Springs, California
February 28, 2019

## Slide 2: Colorado River – Operational Setting
16.5 million acre-feet (maf) allocated annually
  7.5 maf each to Upper and Lower Basins
  1.5 maf to Mexico
~ 16 maf average annual “natural flow” (from historical record)
  14.8 maf in the Upper Basin and 1.3 maf in the Lower Basin
Inflows are highly variable year to year
60 maf of storage (~ 4 times the annual average inflow)
Operations and water deliveries governed by the “Law of the River”

## Slide 3
Colorado River Basin
Law of the River
Colorado River Compact, 1922
Boulder Canyon Project Act, 1928
US-Mexico Water Treaty, 1944
Upper Colorado River Basin Compact, 1948
Colorado River Storage Project Act, 1956
Consolidated Supreme Court Decree, Arizona v. California, 1964 (and following)
Colorado River Basin Salinity Control Act, 1974 (and following)
Colorado River Basin Project Act, 1968
5

## Slide 4
Coordinated Operation of Lake Powell and Lake Mead
Lake Powell Filling Criteria, 1962
Long-Range Operating Criteria, 1970 (minor modifications in 2005)
Interim Surplus Guidelines, 2001
602(a) Storage Guideline, 2004
Interim Guidelines for Lower Basin Shortages and Coordinated Operations for Lake Powell and Lake Mead, 2007
6

## Slide 6
State of the System (Water Years 1999-2019)1,2
Notes: 6

## Slide 7
Water Budget at Lake Mead
Given current water demands in the Lower Basin and Mexico, and a minimum objective release from Lake Powell (8.23 maf), Lake Mead storage declines by about 1.2 maf annually (equivalent to about 12 feet in elevation).
  Inflow 9.0 maf Powell release + side inflows above Mead
  Outflow -9.6 maf
  Lower Basin State apportionments and
  Mexico Treaty allocation, plus balance of
  downstream regulation, gains, and losses
  Mead evaporation loss -0.6 maf
  Balance -1.2 maf

## Slide 8: Lake Powell and Lake Mead Operational Diagrams (According to the 2007 Interim Guidelines)
1 Whenever Lake Mead is below elevation 1,025 feet, the Secretary shall consider whether hydrologic conditions together with anticipated deliveries to the Lower Division States and Mexico is likely to cause the elevation at Lake Mead to fall below 1,000 feet. Such consideration, in consultation with the Basin States, may result in the undertaking of further measures, consistent with applicable Federal law.
Lake Mead
Lake Powell
2/23/19: 3,573 feet
9.3 maf (38% Full)
2/23/19: 1,087 feet
10.6 maf (41% Full)

## Slide 9: Upper Colorado River Basin Water Year 2019 Snowpack and Observed Inflow
Colorado River Basin above Lake Powell
Water Year 2019
Precipitation
(year-to-date)
113% of average
Current Snowpack
116% of median
1Percent of normal precipitation is based on an arithmetic mean, or average; percent of normal snowpack is based on the median value for a given date.

## Slide 10
Total Contemplated Lower Basin Volumes (in KAF) 2007 Interim Guidelines, Minute 323, Lower Basin Drought Contingency Plan & Binational Water Scarcity Contingency Plan |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lake Mead Elevation (ft msl) | 2007 Interim Guidelines Shortages |  | Minute 323 Delivery Reductions | Total Combined Reductions | DCP Contributions |  |  | Binational Water Scarcity Contingency Plan Savings | Combined Volumes by Country US: (2007 Interim Guidelines Shortages + DCP Contributions) Mexico: (Minute 323 Delivery Reductions + Binational Water Scarcity Contingency Plan Savings) |  |  |  |  | Total Combined Volumes
 | AZ | NV | Mexico | Lower Basin States + Mexico | AZ | NV | CA | Mexico | AZ Total | NV Total | CA Total | Lower Basin States Total | Mexico Total | Lower Basin States + Mexico
1,090 - >1,075 | 0 | 0 | 0 | 0 | 192 | 8 | 0 | 41 | 192 | 8 | 0 | 200 | 41 | 241
1,075 - >1050 | 320 | 13 | 50 | 383 | 192 | 8 | 0 | 30 | 512 | 21 | 0 | 533 | 80 | 613
1,050 - >1,045 | 400 | 17 | 70 | 487 | 192 | 8 | 0 | 34 | 592 | 25 | 0 | 617 | 104 | 721
1,045 - >1,040 | 400 | 17 | 70 | 487 | 240 | 10 | 200 | 76 | 640 | 27 | 200 | 867 | 146 | 1,013
1,040 - >1,035 | 400 | 17 | 70 | 487 | 240 | 10 | 250 | 84 | 640 | 27 | 250 | 917 | 154 | 1,071
1,035 - >1,030 | 400 | 17 | 70 | 487 | 240 | 10 | 300 | 92 | 640 | 27 | 300 | 967 | 162 | 1,129
1,030 – 1,025 | 400 | 17 | 70 | 487 | 240 | 10 | 350 | 101 | 640 | 27 | 350 | 1,017 | 171 | 1,188
<1,025 | 480 | 20 | 125 | 625 | 240 | 10 | 350 | 150 | 720 | 30 | 350 | 1,100 | 275 | 1,375
The US will work to create or conserve 100,000 af or more of Colorado River system water on an annual basis to contribute to conservation of water supplies in Lake Mead and other Colorado River reservoirs. All actions taken by the United States shall be subject to applicable federal law, including availability of appropriations.

## Slide 11
Attachment A1:
Drought Response Operations Agreement
Attachment A2:
Demand Management Storage Agreement
Colorado River Basin Drought Contingency Plans
*Activates Section IV of Minute 323 (Binational Water Scarcity Contingency Plan)
Exhibit 1:
LB Drought Contingency Operations (LBOps)
Attachment B:
LB DCP Agreement
Agreement Concerning Colorado River Drought Contingency
Management and Operations
(Companion Agreement)
Upper Basin DCP
Lower Basin DCP*
Arizona Agreements
ICS Exhibits
Intra-State DCP Agreements
Legislation
California Agreements
ICS Exhibits
Intra-State DCP Agreements
Nevada Agreements
ICS Exhibits
Federal Legislation

## Slide 15
Thank You!
Jack Simes
Ph. 951-695-5310
jsimes@usbr.gov