## Slide 1: Projections and Uncertainty in the Colorado River Basin
Rebecca Smith, PhD, Lower Colorado Basin Region
Urban Water Institute Conference
September 8, 2021

## Slide 2: Process to Project System Conditions
  System conditions are most sensitive to assumptions about future hydrology
  To account for the uncertainty in future hydrology, multiple, sometimes hundreds, of hydrologic traces are used
  Models are run using each hydrologic trace, resulting in projections of system conditions (e.g. reservoir elevations, releases, etc.)
  For probabilistic projections, statistics are computed to get risk
System Model
Hydrology
Demand
Policy
2. Key sources of uncertainty
3. Run model
4. Project system conditions & compute risks
1. Initial conditions
Initial Reservoir Elevations

## Slide 3: Models, Data, & Assumptions for Different Projection Horizons
Hundreds of hydrology traces available based on historical data and climate projections
Stakeholder-provided Upper & Lower Basin demand projections
Current operating policies applied via rules through 2026, followed by assumptions
Current Conditions
24 months
CRMMS-24MS Mode
2-5 years
CRMMS-ESP Mode
Decades
CRSS
3 hydrology traces based on CBRFC forecasts + historical data
Embedded Upper Basin water use, stakeholder-provided Lower Basin demands
Current operating policies applied via rules and operator expertise
35 hydrology traces based on CBRFC forecasts + historical data
Embedded Upper Basin water use, stakeholder-provided Lower Basin demands
Current operating policies applied via rules
CRMMS = Colorado River Mid-Term Modeling System
CBRFC = Colorado Basin River Forecast Center
ESP = Ensemble Streamflow Prediction
CRSS = Colorado River Simulation System

## Slide 4: Purpose- & Data-Driven Projections
24-Month Study: least uncertainty
  Decisional months capitalize on skillful forecasts and well characterized demands
  Specific projections tied to policy
2- to 5-Year probabilistic projections: moderate to large uncertainty
  Capitalize on moderate forecast skill in Year 1
  Incorporate more information from historical hydrology to explore wider range of potential future system conditions
  Understand possibilities considering current conditions and policies
Decades-long probabilistic projections: deep uncertainty
  Incorporate full range of historical hydrology information, climate change-informed historical information, and climate change projections
  Explore impacts of climate change and different demand and policy assumption for long-term planning

## Slide 5: Upper Colorado River Basin Hydrology
Lees Ferry, AZ, stream gage
  Near 1922 Compact point (Lee Ferry)
  Divides Upper Basin and Lower Basin
Upper Basin accounts for approximately 90% of total CRB streamflow
Highly variable from year to year
Notes: Points to make:
Basin is characterized by highly variable hydrology and we have constructed a large amount of storage to deal with that variability – 4x average annual inflow
Store water in the high flow years so that deliveries can be made in low flow years
As demand has increased over time, our margin has become tighter, particularly in the Lower Basin

## Slide 6
Chart: Year
Provisional 2020-2021 | 17.8469 | 9.1523 | 7.585
Avg Annual Flow 1906-2019: 14.7 maf
Lees Ferry Observed Natural Flow Record (1906-2021)

## Slide 7
Increasing Temperature Trend
Annually-averaged temperature for the Colorado River Basin, 1895–2018, shown as departures from a 1970–1999 average. The gray line is a 10-year running average plotted on the 6th year. A 40-year linear trend (dashed yellow line) shows 2.4°F of warming from 1979–2018. Figure taken from forthcoming Colorado River Basin Climate and Hydrology—State of the Science Report: https://www.usbr.gov/lc/region/programs/research-reports-etc/Final_CRB_SoS_Project_Overview.pdf
Notes: Figure 2.16 Annually-averaged temperature for the Colorado River Basin, 1895–2018, shown as
departures from a 1970–1999 average. The gray line is a 10-year running average plotted on the
6th year. A 40-year linear trend (dashed yellow line) shows 2.4°F of warming from 1979–2018.
It’s been getting hotter since the 80s and we know that hotter temps result in less streamflow for a given amount of precipitation. Let’s take the recently observed streamflow and leave off most of the observations from the cooler 20th century

## Slide 8
Chart: Year
Stress Test 1988-2019 | 15.3342 | 11.1885 | 9.4742 | 9.3509 | 12.3225 | 10.9163 | 18.9161 | 10.581 | 19.9878 | 14.2167 | 21.686 | 16.7035 | 15.8743 | 10.5339 | 10.7259 | 6.0235 | 10.5388 | 9.9289 | 17.1231 | 13.5496 | 11.417 | 16.1217 | 14.1355 | 12.7215 | 20.3027 | 7.8053 | 9.5967 | 14.3616 | 13.0496 | 13.4297 | 16.4207 | 8.3206 | 17.8469
Provisional 2020-2021 | 17.8469 | 9.1523 | 7.585
5-Year Avg | 18.9797 | 16.0032 | 13.6652 | 11.534 | 10.6505 | 12.196 | 12.4174 | 14.5447 | 14.9236 | 17.0775 | 16.635 | 17.6937 | 15.8029 | 15.1047 | 11.9722 | 10.7393 | 9.5502 | 10.868 | 11.4328 | 12.5115 | 13.6281 | 14.4694 | 13.5891 | 14.9397 | 14.2174 | 12.9123 | 12.9575 | 13.0232 | 11.6486 | 13.3717 | 13.1164 | 13.8135
Avg Annual Flow 1988-2019: 13.3 maf
Avg Annual Flow 1906-2019: 14.7 maf
Lees Ferry Observed Natural Flow Record (1906-2021)

## Slide 9
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Aug2020_2021_9011,DNF,2016Dems,NA.9004,Most | 0 | 0 | 0 | 0 | 0.026549 | 0.017699
Aug2020_2021_9011,ISM1988_2018,2016Dems,NA.9004,Most | 0 | 0 | 0 | 0 | 0.096774 | 0.12903
Full Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.026549 | 0.017699
Stress Test Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.096774 | 0.12903
*Projections not official; based on August 2020 CRSS modeling with Lake Powell initial elevation of 3,592’. Lake Powell’s current elevation is ~3,550’
Mid-Term Uncertainty and Shifting Risk*

## Slide 10
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Aug2020_2021_9011,CMIP5,2016Dems,NA.9004,Most | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632
Aug2020_2021_9011,DNF,2016Dems,NA.9004,Most | 0 | 0 | 0 | 0 | 0.026549 | 0.017699
Aug2020_2021_9011,ISM1988_2018,2016Dems,NA.9004,Most | 0 | 0 | 0 | 0 | 0.096774 | 0.12903
CMIP3 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714
CMIP5 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632
Full Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.026549 | 0.017699
Stress Test Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.096774 | 0.12903
** CMIP3 and CMIP5 ensembles span 3 different emissions futures and were downscaled using Bias Correction Spatial Downscaling (BCSD)
*Projections not official; based on August 2020 CRSS modeling with Lake Powell initial elevation of 3,592’. Lake Powell’s current elevation is ~3,550’
Mid-Term Uncertainty and Shifting Risk*

## Slide 11
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Aug2020_2021,ISM1988_2018,2007Dems,NA,Most | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.25806 | 0.29032 | 0.35484 | 0.3871 | 0.35484 | 0.3871 | 0.29032 | 0.3871 | 0.3871 | 0.3871 | 0.41935 | 0.51613 | 0.51613 | 0.54839 | 0.58065 | 0.58065 | 0.54839 | 0.54839 | 0.58065 | 0.70968 | 0.70968 | 0.64516 | 0.67742 | 0.70968
CMIP3 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.11607 | 0.11607 | 0.15179 | 0.13393 | 0.17857 | 0.19643 | 0.23214 | 0.20536 | 0.21429 | 0.24107 | 0.25893 | 0.26786 | 0.26786 | 0.27679 | 0.30357 | 0.30357 | 0.30357 | 0.30357 | 0.34821 | 0.33036 | 0.33036 | 0.35714 | 0.32143 | 0.30357
CMIP5 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632 | 0.065789 | 0.039474 | 0.052632 | 0.092105 | 0.092105 | 0.092105 | 0.052632 | 0.052632 | 0.052632 | 0.052632 | 0.026316 | 0.039474 | 0.052632 | 0.10526 | 0.065789 | 0.078947 | 0.065789 | 0.078947 | 0.078947 | 0.11842 | 0.14474 | 0.11842 | 0.10526 | 0.14474
Full Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.026549 | 0.017699 | 0.0088496 | 0.0088496 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Stress Test Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.096774 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.096774 | 0.096774 | 0.12903 | 0.096774 | 0.12903 | 0.12903 | 0.096774 | 0.16129 | 0.12903 | 0.16129 | 0.19355 | 0.19355 | 0.19355 | 0.19355 | 0.22581 | 0.25806 | 0.25806 | 0.25806 | 0.29032 | 0.25806
Stress Test Hydrology; Alternative Demands; Current Policies Continue | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.19355 | 0.22581 | 0.19355 | 0.19355 | 0.25806 | 0.3871 | 0.35484 | 0.32258 | 0.29032 | 0.29032 | 0.32258 | 0.29032 | 0.29032 | 0.29032 | 0.32258 | 0.32258 | 0.32258
Long-term risk outlooks using different supply, demand, and policy assumptions*
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Aug2020_2021,ISM1988_2018,2007Dems,NA,Most | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.25806 | 0.29032 | 0.35484 | 0.3871 | 0.35484 | 0.3871 | 0.29032 | 0.3871 | 0.3871 | 0.3871 | 0.41935 | 0.51613 | 0.51613 | 0.54839 | 0.58065 | 0.58065 | 0.54839 | 0.54839 | 0.58065 | 0.70968 | 0.70968 | 0.64516 | 0.67742 | 0.70968
CMIP3 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.11607 | 0.11607 | 0.15179 | 0.13393 | 0.17857 | 0.19643 | 0.23214 | 0.20536 | 0.21429 | 0.24107 | 0.25893 | 0.26786 | 0.26786 | 0.27679 | 0.30357 | 0.30357 | 0.30357 | 0.30357 | 0.34821 | 0.33036 | 0.33036 | 0.35714 | 0.32143 | 0.30357
CMIP5 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632 | 0.065789 | 0.039474 | 0.052632 | 0.092105 | 0.092105 | 0.092105 | 0.052632 | 0.052632 | 0.052632 | 0.052632 | 0.026316 | 0.039474 | 0.052632 | 0.10526 | 0.065789 | 0.078947 | 0.065789 | 0.078947 | 0.078947 | 0.11842 | 0.14474 | 0.11842 | 0.10526 | 0.14474
Full Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.026549 | 0.017699 | 0.0088496 | 0.0088496 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Stress Test Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.096774 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.096774 | 0.096774 | 0.12903 | 0.096774 | 0.12903 | 0.12903 | 0.096774 | 0.16129 | 0.12903 | 0.16129 | 0.19355 | 0.19355 | 0.19355 | 0.19355 | 0.22581 | 0.25806 | 0.25806 | 0.25806 | 0.29032 | 0.25806
** CMIP3 and CMIP5 ensembles span 3 different emissions futures and were downscaled using Bias Correction Spatial Downscaling (BCSD)
*Projections not official; based on August 2020 CRSS modeling with Lake Powell initial elevation of 3,592’. Lake Powell’s current elevation is ~3,550’

## Slide 12
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Aug2020_2021,ISM1988_2018,2007Dems,NA,Most | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.25806 | 0.29032 | 0.35484 | 0.3871 | 0.35484 | 0.3871 | 0.29032 | 0.3871 | 0.3871 | 0.3871 | 0.41935 | 0.51613 | 0.51613 | 0.54839 | 0.58065 | 0.58065 | 0.54839 | 0.54839 | 0.58065 | 0.70968 | 0.70968 | 0.64516 | 0.67742 | 0.70968
CMIP3 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.11607 | 0.11607 | 0.15179 | 0.13393 | 0.17857 | 0.19643 | 0.23214 | 0.20536 | 0.21429 | 0.24107 | 0.25893 | 0.26786 | 0.26786 | 0.27679 | 0.30357 | 0.30357 | 0.30357 | 0.30357 | 0.34821 | 0.33036 | 0.33036 | 0.35714 | 0.32143 | 0.30357
CMIP3 Hydrology; 2016 Demands; Policy Shifts to No Action Alternative | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.125 | 0.19643 | 0.23214 | 0.22321 | 0.24107 | 0.24107 | 0.27679 | 0.29464 | 0.28571 | 0.29464 | 0.28571 | 0.3125 | 0.3125 | 0.32143 | 0.34821 | 0.3125 | 0.33929 | 0.34821 | 0.375 | 0.35714 | 0.3125 | 0.375 | 0.32143 | 0.3125
CMIP5 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632 | 0.065789 | 0.039474 | 0.052632 | 0.092105 | 0.092105 | 0.092105 | 0.052632 | 0.052632 | 0.052632 | 0.052632 | 0.026316 | 0.039474 | 0.052632 | 0.10526 | 0.065789 | 0.078947 | 0.065789 | 0.078947 | 0.078947 | 0.11842 | 0.14474 | 0.11842 | 0.10526 | 0.14474
Full Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.026549 | 0.017699 | 0.0088496 | 0.0088496 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Stress Test Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.096774 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.096774 | 0.096774 | 0.12903 | 0.096774 | 0.12903 | 0.12903 | 0.096774 | 0.16129 | 0.12903 | 0.16129 | 0.19355 | 0.19355 | 0.19355 | 0.19355 | 0.22581 | 0.25806 | 0.25806 | 0.25806 | 0.29032 | 0.25806
Stress Test Hydrology; Alternative Demands; Current Policies Continue | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.19355 | 0.22581 | 0.19355 | 0.19355 | 0.25806 | 0.3871 | 0.35484 | 0.32258 | 0.29032 | 0.29032 | 0.32258 | 0.29032 | 0.29032 | 0.29032 | 0.32258 | 0.32258 | 0.32258
Long-term risk outlooks using different supply, demand, and policy assumptions*
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Aug2020_2021,ISM1988_2018,2007Dems,NA,Most | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.25806 | 0.29032 | 0.35484 | 0.3871 | 0.35484 | 0.3871 | 0.29032 | 0.3871 | 0.3871 | 0.3871 | 0.41935 | 0.51613 | 0.51613 | 0.54839 | 0.58065 | 0.58065 | 0.54839 | 0.54839 | 0.58065 | 0.70968 | 0.70968 | 0.64516 | 0.67742 | 0.70968
CMIP3 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.11607 | 0.11607 | 0.15179 | 0.13393 | 0.17857 | 0.19643 | 0.23214 | 0.20536 | 0.21429 | 0.24107 | 0.25893 | 0.26786 | 0.26786 | 0.27679 | 0.30357 | 0.30357 | 0.30357 | 0.30357 | 0.34821 | 0.33036 | 0.33036 | 0.35714 | 0.32143 | 0.30357
CMIP3 Hydrology; 2016 Demands; Policy Shifts to No Action Alternative | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.125 | 0.19643 | 0.23214 | 0.22321 | 0.24107 | 0.24107 | 0.27679 | 0.29464 | 0.28571 | 0.29464 | 0.28571 | 0.3125 | 0.3125 | 0.32143 | 0.34821 | 0.3125 | 0.33929 | 0.34821 | 0.375 | 0.35714 | 0.3125 | 0.375 | 0.32143 | 0.3125
CMIP5 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632 | 0.065789 | 0.039474 | 0.052632 | 0.092105 | 0.092105 | 0.092105 | 0.052632 | 0.052632 | 0.052632 | 0.052632 | 0.026316 | 0.039474 | 0.052632 | 0.10526 | 0.065789 | 0.078947 | 0.065789 | 0.078947 | 0.078947 | 0.11842 | 0.14474 | 0.11842 | 0.10526 | 0.14474
Full Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.026549 | 0.017699 | 0.0088496 | 0.0088496 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Stress Test Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.096774 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.096774 | 0.096774 | 0.12903 | 0.096774 | 0.12903 | 0.12903 | 0.096774 | 0.16129 | 0.12903 | 0.16129 | 0.19355 | 0.19355 | 0.19355 | 0.19355 | 0.22581 | 0.25806 | 0.25806 | 0.25806 | 0.29032 | 0.25806
Stress Test Hydrology; Alternative Demands; Current Policies Continue | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.19355 | 0.22581 | 0.19355 | 0.19355 | 0.25806 | 0.3871 | 0.35484 | 0.32258 | 0.29032 | 0.29032 | 0.32258 | 0.29032 | 0.29032 | 0.29032 | 0.32258 | 0.32258 | 0.32258
*Projections not official; based on August 2020 CRSS modeling with Lake Powell initial elevation of 3,592’. Lake Powell’s current elevation is ~3,550’
** CMIP3 and CMIP5 ensembles span 3 different emissions futures and were downscaled using Bias Correction Spatial Downscaling (BCSD)
Notes: Demands and policy are also uncertain
Note that risk has shifted dramatically since last year- powell is over 40 ft lower

## Slide 13
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Aug2020_2021,ISM1988_2018,2007Dems,NA,Most | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.25806 | 0.29032 | 0.35484 | 0.3871 | 0.35484 | 0.3871 | 0.29032 | 0.3871 | 0.3871 | 0.3871 | 0.41935 | 0.51613 | 0.51613 | 0.54839 | 0.58065 | 0.58065 | 0.54839 | 0.54839 | 0.58065 | 0.70968 | 0.70968 | 0.64516 | 0.67742 | 0.70968
CMIP3 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.11607 | 0.11607 | 0.15179 | 0.13393 | 0.17857 | 0.19643 | 0.23214 | 0.20536 | 0.21429 | 0.24107 | 0.25893 | 0.26786 | 0.26786 | 0.27679 | 0.30357 | 0.30357 | 0.30357 | 0.30357 | 0.34821 | 0.33036 | 0.33036 | 0.35714 | 0.32143 | 0.30357
CMIP3 Hydrology; 2016 Demands; Policy Shifts to No Action Alternative | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.125 | 0.19643 | 0.23214 | 0.22321 | 0.24107 | 0.24107 | 0.27679 | 0.29464 | 0.28571 | 0.29464 | 0.28571 | 0.3125 | 0.3125 | 0.32143 | 0.34821 | 0.3125 | 0.33929 | 0.34821 | 0.375 | 0.35714 | 0.3125 | 0.375 | 0.32143 | 0.3125
CMIP5 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632 | 0.065789 | 0.039474 | 0.052632 | 0.092105 | 0.092105 | 0.092105 | 0.052632 | 0.052632 | 0.052632 | 0.052632 | 0.026316 | 0.039474 | 0.052632 | 0.10526 | 0.065789 | 0.078947 | 0.065789 | 0.078947 | 0.078947 | 0.11842 | 0.14474 | 0.11842 | 0.10526 | 0.14474
Full Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.026549 | 0.017699 | 0.0088496 | 0.0088496 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0088496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Stress Test Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0 | 0 | 0.096774 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.12903 | 0.096774 | 0.096774 | 0.12903 | 0.096774 | 0.12903 | 0.12903 | 0.096774 | 0.16129 | 0.12903 | 0.16129 | 0.19355 | 0.19355 | 0.19355 | 0.19355 | 0.22581 | 0.25806 | 0.25806 | 0.25806 | 0.29032 | 0.25806
Stress Test Hydrology; Alternative Demands; Current Policies Continue | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.16129 | 0.19355 | 0.16129 | 0.19355 | 0.22581 | 0.19355 | 0.19355 | 0.25806 | 0.3871 | 0.35484 | 0.32258 | 0.29032 | 0.29032 | 0.32258 | 0.29032 | 0.29032 | 0.29032 | 0.32258 | 0.32258 | 0.32258
Long-term risk outlooks using different supply, demand, and policy assumptions*
Chart: Lake Powell < 3,490 Feet in Any Month
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Aug2020_2021,CMIP3,2007Dems,IG_DCP,Most | 0 | 0 | 0.017857 | 0.035714 | 0.080357 | 0.10714 | 0.13393 | 0.16071 | 0.22321 | 0.21429 | 0.23214 | 0.22321 | 0.26786 | 0.26786 | 0.25 | 0.30357 | 0.30357 | 0.30357 | 0.29464 | 0.30357 | 0.34821 | 0.32143 | 0.33929 | 0.34821 | 0.375 | 0.35714 | 0.36607 | 0.375 | 0.34821 | 0.33036
Aug2020_2021,CMIP3,2007Dems,NA,Most | 0 | 0 | 0.017857 | 0.035714 | 0.080357 | 0.10714 | 0.16071 | 0.27679 | 0.29464 | 0.29464 | 0.32143 | 0.3125 | 0.3125 | 0.33036 | 0.33036 | 0.35714 | 0.33036 | 0.375 | 0.35714 | 0.36607 | 0.39286 | 0.35714 | 0.35714 | 0.375 | 0.39286 | 0.36607 | 0.35714 | 0.39286 | 0.35714 | 0.36607
Aug2020_2021,CMIP5,2007Dems,IG_DCP,Most | 0 | 0 | 0.013158 | 0.013158 | 0.052632 | 0.065789 | 0.065789 | 0.052632 | 0.065789 | 0.10526 | 0.092105 | 0.10526 | 0.065789 | 0.078947 | 0.065789 | 0.11842 | 0.10526 | 0.078947 | 0.10526 | 0.11842 | 0.10526 | 0.10526 | 0.10526 | 0.10526 | 0.14474 | 0.17105 | 0.15789 | 0.13158 | 0.11842 | 0.15789
Aug2020_2021,CMIP5,2007Dems,NA,Most | 0 | 0 | 0.013158 | 0.013158 | 0.052632 | 0.065789 | 0.078947 | 0.10526 | 0.10526 | 0.14474 | 0.13158 | 0.10526 | 0.11842 | 0.11842 | 0.13158 | 0.13158 | 0.14474 | 0.11842 | 0.13158 | 0.13158 | 0.15789 | 0.15789 | 0.15789 | 0.14474 | 0.15789 | 0.19737 | 0.18421 | 0.15789 | 0.15789 | 0.17105
Aug2020_2021,DNF,2007Dems,IG_DCP,Most | 0 | 0 | 0 | 0.0088496 | 0.026549 | 0.035398 | 0.026549 | 0.0088496 | 0.0088496 | 0.0088496 | 0 | 0.017699 | 0.0088496 | 0 | 0.035398 | 0.026549 | 0.026549 | 0.061947 | 0.044248 | 0.044248 | 0.044248 | 0.017699 | 0.026549 | 0.026549 | 0.026549 | 0.053097 | 0.026549 | 0.0088496 | 0.017699 | 0.035398
Aug2020_2021,DNF,2007Dems,NA,Most | 0 | 0 | 0 | 0.0088496 | 0.026549 | 0.035398 | 0.044248 | 0.079646 | 0.070796 | 0.10619 | 0.097345 | 0.097345 | 0.079646 | 0.10619 | 0.12389 | 0.10619 | 0.13274 | 0.14159 | 0.17699 | 0.17699 | 0.17699 | 0.17699 | 0.14159 | 0.15044 | 0.14159 | 0.15929 | 0.15044 | 0.15044 | 0.15929 | 0.15044
Aug2020_2021,ISM1988_2018,2007Dems,NA,Most | 0 | 0 | 0 | 0.064516 | 0.096774 | 0.12903 | 0.25806 | 0.29032 | 0.35484 | 0.3871 | 0.35484 | 0.3871 | 0.29032 | 0.3871 | 0.3871 | 0.3871 | 0.41935 | 0.51613 | 0.51613 | 0.54839 | 0.58065 | 0.58065 | 0.54839 | 0.54839 | 0.58065 | 0.70968 | 0.70968 | 0.64516 | 0.67742 | 0.70968
Aug2020_2021_9011,CMIP5,2016Dems,NA.9004,Most | 0 | 0 | 0.013158 | 0 | 0.026316 | 0.052632 | 0.065789 | 0.078947 | 0.10526 | 0.11842 | 0.11842 | 0.10526 | 0.078947 | 0.078947 | 0.092105 | 0.092105 | 0.092105 | 0.078947 | 0.11842 | 0.11842 | 0.11842 | 0.13158 | 0.13158 | 0.13158 | 0.15789 | 0.14474 | 0.15789 | 0.13158 | 0.13158 | 0.15789
Aug2020_2021_9011,DNF,2016Dems,NA.9004,Most | 0 | 0 | 0 | 0 | 0.026549 | 0.017699 | 0.017699 | 0.044248 | 0.035398 | 0.017699 | 0.035398 | 0.035398 | 0.026549 | 0.0088496 | 0.035398 | 0.053097 | 0.053097 | 0.061947 | 0.053097 | 0.070796 | 0.053097 | 0.035398 | 0.035398 | 0.035398 | 0.035398 | 0.053097 | 0.044248 | 0.053097 | 0.053097 | 0.044248
Aug2020_2021_9011,ISM1988_2018,2016Dems,NA.9004,Most | 0 | 0 | 0 | 0 | 0.096774 | 0.12903 | 0.16129 | 0.16129 | 0.22581 | 0.22581 | 0.25806 | 0.25806 | 0.25806 | 0.25806 | 0.29032 | 0.22581 | 0.32258 | 0.32258 | 0.35484 | 0.32258 | 0.32258 | 0.25806 | 0.32258 | 0.32258 | 0.35484 | 0.3871 | 0.3871 | 0.41935 | 0.41935 | 0.41935
CMIP3 Hydrology; 2016 Demands; Current Policies Continue | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.11607 | 0.11607 | 0.15179 | 0.13393 | 0.17857 | 0.19643 | 0.23214 | 0.20536 | 0.21429 | 0.24107 | 0.25893 | 0.26786 | 0.26786 | 0.27679 | 0.30357 | 0.30357 | 0.30357 | 0.30357 | 0.34821 | 0.33036 | 0.33036 | 0.35714 | 0.32143 | 0.30357
CMIP3 Hydrology; 2016 Demands; Policy Shifts to No Action Alternative | 0 | 0 | 0.017857 | 0.035714 | 0.071429 | 0.10714 | 0.125 | 0.19643 | 0.23214 | 0.22321 | 0.24107 | 0.24107 | 0.27679 | 0.29464 | 0.28571 | 0.29464 | 0.28571 | 0.3125 | 0.3125 | 0.32143 | 0.34821 | 0.3125 | 0.33929 | 0.34821 | 0.375 | 0.35714 | 0.3125 | 0.375 | 0.32143 | 0.3125
*Projections not official; based on August 2020 CRSS modeling with Lake Powell initial elevation of 3,592’. Lake Powell’s current elevation is ~3,550’
** CMIP3 and CMIP5 ensembles span 3 different emissions futures and were downscaled using Bias Correction Spatial Downscaling (BCSD)
Notes: Demands and policy are also uncertain
Note that risk has shifted dramatically since last year- powell is over 40 ft lower

## Slide 14
Long-Term Planning under Deep Uncertainty
Deep uncertainty occurs when probabilities of any given set of future conditions cannot be estimated with confidence
  Translation: it is impossible to determine the most appropriate planning assumptions
Statistics-based analysis (e.g. “percent of traces”, “acceptable risk”) may be unreliable as the sole basis for understanding system or planning for future
Decision Making under Deep Uncertainty (DMDU) planning methods incorporate concepts and techniques that help address the challenges of planning under climate change
  Seeking robust solutions that perform well enough in a wide range of future conditions
  Characterize vulnerabilities based on observable conditions
  Plan for adaptation as conditions evolve (and uncertainty decreases)

## Slide 15
Thank You
Rebecca Smith: rebeccasmith@usbr.gov